## Slide 1: Cryptography and Network Security
Eighth Edition
by William Stallings
Notes: Lecture slides prepared for “Cryptography and Network Security”, 8/e, by William Stallings, Chapter 23 – “Internet of Things (IoT) Security”.

## Slide 2: Chapter 23
Internet of Things (IoT) Security
Notes: This chapter begins with an overview of the concepts of the IoT, followed by a discussion of IoT security.

## Slide 3: The Internet of Things
The Internet of Things (IoT) is a term that refers to the expanding interconnection of smart devices
A dominant theme is the embedding of short-range mobile transceivers into a wide array of gadgets and everyday items, enabling new forms of communication between people and things, and between things themselves
The Internet now supports the interconnection of billions of industrial and personal objects, usually through cloud systems
The objects deliver sensor information, act on their environment, and in some cases modify themselves, to create overall management of a larger system
Notes: The Internet of Things (IoT) is a term that refers to the expanding interconnection of smart devices, ranging from appliances to tiny sensors. A dominant theme is the embedding of short-range mobile transceivers into a wide array of gadgets and everyday items, enabling new forms of communication between people and things, and between things themselves. The Internet now supports the interconnection of billions of industrial and personal objects, usually through cloud systems. The objects deliver sensor information, act on their environment, and in some cases modify themselves, to create overall management of a larger system, like a factory or city.

## Slide 4: IoT
The IoT is primarily driven by deeply embedded devices
These devices are low-bandwidth, low-repetition data capture and low-bandwidth data-usage appliances that communicate with each other and provide data via user interfaces
Embedded appliances, such as high-resolution video security cameras, video VoIP phones, and a handful of others, require high-bandwidth streaming capabilities
Countless products simply require packets of data to be intermittently delivered
Notes: The IoT is primarily driven by deeply embedded devices. These devices are low-bandwidth, low-repetition data capture and low-bandwidth data-usage appliances that communicate with each other and provide data via user interfaces. Embedded appliances, such as high-resolution video security cameras, video VoIP phones, and a handful of others, require high-bandwidth streaming capabilities. Yet countless products simply require packets of data to be intermittently delivered.

## Slide 5: Evolution
The Internet has gone through roughly four generations of deployment culminating in the IoT:
    Information technology (IT): PCs, servers, routers, firewalls, and so on, bought as IT devices by enterprise IT people, primarily using wired connectivity
    Operational technology (OT): Machines/appliances with embedded IT built by non-IT companies, such as medical machinery, SCADA (supervisory control and data acquisition), process control, and kiosks, bought as appliances by enterprise OT people and primarily using wired connectivity
    Personal technology: Smartphones, tablets, and eBook readers bought as IT devices by consumers (employees) exclusively using wireless connectivity and often multiple forms of wireless connectivity
    Sensor/actuator technology: Single-purpose devices bought by consumers, IT, and OT people exclusively using wireless connectivity, generally of a single form, as part of larger systems
It is the fourth generation that is usually thought of as the IoT, and which is marked by the use of billions of embedded devices
Notes: With reference to the end systems supported, the Internet has gone through roughly four generations of deployment culminating in the IoT:
Information technology (IT): PCs, servers, routers, firewalls, and so on, bought as IT devices by enterprise IT people, primarily using wired connectivity.
Operational technology (OT): Machines/appliances with embedded IT built by non-IT companies, such as medical machinery, SCADA (supervisory control and data acquisition), process control, and kiosks, bought as appliances by enterprise OT people and primarily using wired connectivity.
Personal technology: Smartphones, tablets, and eBook readers bought as IT devices by consumers (employees) exclusively using wireless connectivity and often multiple forms of wireless connectivity.
Sensor/actuator technology: Single-purpose devices bought by consumers, IT, and OT people exclusively using wireless connectivity, generally of a single form, as part of larger systems.
It is the fourth generation that is usually thought of as the IoT, and which is marked by the use of billions of embedded devices.

## Slide 6
Notes: The key components of an IoT-enabled device are the following (Figure 23.1):
Sensor: A sensor measures some parameter of a physical, chemical, or biological entity and delivers an electronic signal proportional to the observed characteristic, either in the form of an analog voltage level or a digital signal. In both cases, the sensor output is typically input to a microcontroller or other management element.
Actuator: An actuator receives an electronic signal from a controller and responds by interacting with its environment to produce an effect on some parameter of a physical, chemical, or biological entity.
Microcontroller: The “smart” in a smart device is provided by a deeply embedded microcontroller.
Transceiver: A transceiver contains the electronics needed to transmit and receive data. Most IoT devices contain a wireless transceiver, capable of communication using Wi-Fi, ZigBee, or some other wireless scheme.
Power supply: Typically, this is a battery.

## Slide 7: IoT and RFID
Radio-Frequency Identification (RFID)
RFID technology, which uses radio waves to identify items, is increasingly becoming an enabling technology for IoT
The main elements of an RFID system are tags and readers
    RFID tags are small programmable devices used for object, animal, and human tracking
      They come in a variety of shapes, sizes, functionalities, and costs
    RFID readers acquire and sometimes rewrite information stored on RFID tags that come within operating range
      Readers are usually connected to a computer system that records and formats the acquired information for further uses
Notes: IoT devices also often contain a Radio-Frequency Identification (RFID) component. RFID technology, which uses radio waves to identify items, is increasingly becoming an enabling technology for IoT. The main elements of an RFID system are tags and readers. RFID tags are small programmable devices used for object, animal, and human tracking. They come in a variety of shapes, sizes, functionalities, and costs. RFID readers acquire and sometimes rewrite information stored on RFID tags that come within operating range (a few inches up to several feet). Readers are usually connected to a computer system that records and formats the acquired information for further uses.

## Slide 8
Notes: To better understand the function of an IoT, it is useful to view it in the context of a complete enterprise network that includes third-party networking and cloud computing elements. Figure 23.2 provides an overview illustration.

## Slide 9: Edge
At the edge of a typical enterprise network is a network of IoT-enabled devices, consisting of sensors and perhaps actuators
    These devices may communicate with one another
A gateway interconnects the IoT-enabled devices with the higher-level communication networks
    It performs the necessary translation between the protocols used in the communication networks and those used by devices
    It may also perform a basic data aggregation function
Notes: At the edge of a typical enterprise network is a network of IoT-enabled devices, consisting of sensors and perhaps actuators. These devices may communicate with one another. For example, a cluster of sensors may all transmit their data to one sensor that aggregates the data to be collected by a higher-level entity. At this level also there may also be a number of gateways. A gateway interconnects the IoT-enabled devices with the higher-level communication networks. It performs the necessary translation between the protocols used in the communication networks and those used by devices. It may also perform a basic data aggregation function.

## Slide 10: Fog
In many IoT deployments, massive amounts of data may be generated by a distributed network of sensors
Rather than store all of that data permanently (or at least for a long period) in central storage accessible to IoT applications, it is often desirable to do as much data processing close to the sensors as possible
The purpose of what is sometimes referred to as the edge computing level is to convert network data flows into information that is suitable for storage and higher level processing
Processing elements at these level may deal with high volumes of data and perform data transformation operations, resulting in the storage of much lower volumes of data
Notes: In many IoT deployments, massive amounts of data may be generated by a distributed network of sensors. For example, offshore oil fields and refineries can generate a terabyte of data per day. An airplane can create multiple terabytes of data per hour. Rather than store all of that data permanently (or at least for a long period) in central storage accessible to IoT applications, it is often desirable to do as much data processing close to the sensors as possible. Thus, the purpose of what is sometimes referred to as the edge computing level is to convert network data flows into information that is suitable for storage and higher level processing. Processing elements at this level may deal with high volumes of data and perform data transformation operations, resulting in the storage of much lower volumes of data.

## Slide 11: Fog
The following are examples of fog computing operations:
Evaluation: Evaluating data for criteria as to whether it should be processed at a higher level
Formatting: Reformatting data for consistent higher-level processing
Expanding/decoding: Handling cryptic data with additional context (such as the origin)
Distillation/reduction: Reducing and/or summarizing data to minimize the impact of data and traffic on the network and higher-level processing systems
Assessment: Determining whether data represents a threshold or alert; this could include redirecting data to additional destinations
Notes: The following are examples of fog computing operations:
■ Evaluation: Evaluating data for criteria as to whether it should be processed at a higher level.
■ Formatting: Reformatting data for consistent higher-level processing.
■ Expanding/decoding: Handling cryptic data with additional context (such as the origin).
■ Distillation/reduction: Reducing and/or summarizing data to minimize the impact of data and traffic on the network and higher-level processing systems.
■ Assessment: Determining whether data represents a threshold or alert; this could include redirecting data to additional destinations.
Generally, fog computing devices are deployed physically near the edge of the IoT network; that is, near the sensors and other data-generating devices. Thus, some of the basic processing of large volumes of generated data is offloaded and outsourced from IoT application software located at the center.
Fog computing and fog services are expected to be a distinguishing characteristic of the IoT. Fog computing represents an opposite trend in modern networking from cloud computing. With cloud computing, massive, centralized storage and processing resources are made available to distributed customers over cloud networking facilities to a relatively small number of users. With fog computing, massive numbers of individual smart objects are interconnected with fog networking facilities that provide processing and storage resources close to the edge devices in an IoT. Fog computing addresses the challenges raised by the activity of thousands or millions of smart devices, including security, privacy, network capacity constraints, and latency requirements. The term fog computing is inspired by the fact that fog tends to hover low to the ground whereas clouds are high in the sky.

## Slide 12: Core
The core network, also referred to as a backbone network, connects geographically dispersed fog networks as well as provides access to other networks that are not part of the enterprise network
Typically, the core network will use very high performance routers, high-capacity transmission lines, and multiple interconnected routers for increased redundancy and capacity
The core network may also connect to high-performance, high-capacity servers, such as large database servers and private cloud facilities
Some of the core routers may be purely internal, providing redundancy and additional capacity without serving as edge routers
Notes: The core network, also referred to as a backbone network, connects geographically dispersed fog networks as well as provides access to other networks that are not part of the enterprise network. Typically, the core network will use very high performance routers, high-capacity transmission lines, and multiple interconnected routers for increased redundancy and capacity. The core network may also connect to high-performance, high-capacity servers, such as large data- base servers and private cloud facilities. Some of the core routers may be purely internal, providing redundancy and additional capacity without serving as edge routers.

## Slide 13: Cloud
The cloud network provides storage and processing capabilities for the massive amounts of aggregated data that originate in IoT-enabled devices at the edge
Cloud servers also host the applications that interact with and manage the IoT devices and that analyze the IoT-generated data
Notes: The cloud network provides storage and processing capabilities for the massive amounts of aggregated data that originate in IoT-enabled devices at the edge. Cloud servers also host the applications that interact with and manage the IoT devices and that analyze the IoT-generated data.

## Slide 14
(Table is on page 712 in the textbook)
Notes: Table 23.1 compares cloud and fog computing.

## Slide 15
Notes: IoT is perhaps the most complex and undeveloped area of network security. To see this, consider Figure 23.3, which shows the main elements of interest for IoT security. At the center of the network are the application platforms, data storage servers, and network and security management systems. These central systems gather data from sensors, send control signals to actuators, and are responsible for managing the IoT devices and their communication networks. At the edge of the network are IoT-enable devices, some of which are quite simple, constrained devices and some of which are more intelligent, unconstrained devices. In addition, gateways may perform protocol conversion and other networking service on behalf of IoT devices.
Figure 23.3 illustrates a number of typical scenarios for interconnection and the inclusion of security features. The shading in Figure 23.3 indicates the systems that support at least some of these functions. Typically, gateways will implement secure functions, such as TLS and IPsec. Unconstrained devices may or may not implement some security capability. Constrained devices generally have limited or no security features. As suggested in the figure, gateway devices can provide secure communication between the gateway and the devices at the center, such as application platforms and management platforms. However, any constrained or unconstrained devices attached to the gateway are outside the zone of security established between the gateway and the central systems. As shown, unconstrained devices can communicate directly with the center and support security functions. However, constrained devices that are not connected to gateways have no secure communications with central devices.

## Slide 16: Development Issues
Very large attack surfaces
Limited device resources
Complex ecosystem
Fragmentation of standards and regulations
Widespread deployment
Security integration
Safety aspects
Low cost
Lack of expertise
Security updates
Insecure programming
Unclear liabilities
Notes: The European Union Agency For Network And Information Security (ENISA) Baseline Security Recommendations for IoT [ENIS17] lists the following issues that hinder the development of secure IoT ecosystems:
■ Very large attack surfaces: This topic is explored later in this section. In essence, there are a wide variety of points of vulnerability within an IoT ecosystem and a large variety of data that may be compromised.
■ Limited device resources: IoT devices are typically constrained devices, with limited memory, processing power, and power supply.
This makes it difficult to employ advanced security controls.
■ Complex ecosystem: The IoT involves not only a large number of devices, but the interconnections, communications, and dependencies among them and with cloud elements. This makes the task of assessing security risk extremely complex.
■ Fragmentation of standards and regulations: Comparatively little work has been done on security standards for IoT, as well as limited best practices documentation. Thus, there is a lack of comprehensive guidance for security managers and implementers.
■ Widespread deployment: There is an ongoing rapid deployment of IoT arrangements in commercial environments and, more importantly, critical infrastructure environments. These deployments are attractive targets for security attacks and the rapid deployment is often without comprehensive risk assessment and security planning.
■ Security integration: IoT devices use a wide variety of communications protocols, and when implemented, authentication schemes. In addition, there may be contractor viewpoints and requirements from all involved stakeholders. Integrating security into an interoperable scheme is thus extraordinarily challenging.
■ Safety aspects: Because many IoT devices act on their physical environment, security threats can become safety threats, raising the bar for the effectiveness of security solutions.
■ Low cost: IoT devices are manufactured, purchased, and deployed in millions. This provides great incentive for all parties to minimize the cost of these devices. Manufacturers might be inclined to limit security features to maintain a low cost, and customers might be inclined to accept these limitations.
■ Lack of expertise: IoT is still a relatively new and rapidly evolving technology. There are a limited number of people with suitable cybersecurity training and experience.
■ Security updates: In an often-quoted 2014 article, security expert Bruce Schneier stated that we are at a crisis point with regard to the security of embedded systems, including IoT devices [SCHN14]. The embedded devices are riddled with vulnerabilities and there is no good way to patch them. The chip manufacturers have strong incentives to produce their product with its firmware and software as quickly and cheaply as possible. The device manufacturers choose a chip based on price and features and do very little if anything to the chip software and firmware. Their focus is the functionality of the device itself. The end user may have no means of patching the system or, if so, little information about when and how to patch. The result is that the hundreds of millions of Internet-connected devices in the IoT are vulnerable to attack. This is certainly a problem with sensors, allowing attackers to insert false data into the network. It is potentially a graver threat with actuators, where the attacker can affect the operation of machinery and other devices.
■ Insecure programming: Effective cybersecurity practice requires the integration of security planning and design throughout the software development lifecycle. But again, with cost pressure, developers of IoT products have an incentive to place more emphasis on functionality and usability than on security.
■ Unclear liabilities: A major IoT deployment involves a large and complex supply chain and complex interaction among numerous components. Because it is difficult under these circumstances to clearly assign liabilities, ambiguities and conflicts may arise in the event of a security incident.

## Slide 17: IoT Security Objectives
Restricting logical access to the IoT network
    This may include: using unidirectional gateways, using firewalls to prevent network traffic from passing directly between the corporate and IoT networks, and having separate authentication mechanisms and credentials for users of the corporate and IoT networks
    An IoT system should also use a network topology that has multiple layers, with the most critical communications occurring in the most secure and reliable layer
Restricting physical access to IoT network and components
    A combination of physical access controls should be used, such as locks, card readers, and/or guards
Notes: NISTIR 8200 (Interagency Report on Status of International Cybersecurity Standardization for the Internet of Things) lists the following security objectives for IoT:
  ■ Restricting logical access to the IoT network. This may include: using unidirectional gateways, using firewalls to prevent network traffic from passing directly between the corporate and IoT networks, and having separate authentication mechanisms and credentials for users of the corporate and IoT networks. An IoT system should also use a network topology that has multiple layers, with the most critical communications occurring in the most secure and reliable layer.
  ■ Restricting physical access to IoT network and components. A combination of physical access controls should be used, such as locks, card readers, and/or guards.
  ■ Protecting individual IoT components from exploitation. This includes deploying security patches in as expeditious a manner as possible, after testing them under field conditions; disabling all unused ports and services and assuring that they remain disabled; restricting IoT user privileges to only those that are required for each person’s role; tracking and monitoring audit trails; and using security controls such as antivirus software and file integrity checking software where technically feasible.
  ■ Preventing unauthorized modification of data. This includes data that are in transit (at least across the network boundaries) and at rest.
  ■ Detecting security events and incidents. The object is to security events early enough to break the attack chain before attackers attain their objectives. This includes the capability to detect failed IoT components, unavailable services, and exhausted resources that are important to provide proper and safe functioning of an IoT system.
  ■ Maintaining functionality during adverse conditions. This involves designing IoT system so that each critical component has a redundant counterpart. Additionally, if a component fails, it should fail in a manner that does not generate unnecessary traffic on IoT or other networks, or does not cause another problem elsewhere. IoT system should also allow for graceful degradation such as moving from normal operation with full automation to emergency operation with operators more involved and less automation to manual operation with no automation.
  ■ Restoring the system after an incident. Incidents are inevitable and an incident response plan is essential. A major characteristic of a good security program is how quickly the IoT system can be recovered after an incident has occurred.

## Slide 18: IoT Security Objectives
Protecting individual IoT components from exploitation
    This includes deploying security patches in as expeditious a manner as possible, after testing them under field conditions; disabling all unused ports and services and assuring that they remain disabled; restricting IoT user privileges to only those that are required for each person’s role; tracking and monitoring audit trails; and using security controls such as antivirus software and file integrity checking software where technically feasible
Preventing unauthorized modification of data.
    This includes data that are in transit (at least across the network boundaries) and at rest
Detecting security events and incidents
    The object is to detect security events early enough to break the attack chain before attackers attain their objectives. This includes the capability to detect failed IoT components, unavailable services, and exhausted resources that are important to provide proper and safe functioning of an IoT system
Notes: ■ Protecting individual IoT components from exploitation
This includes deploying security patches in as expeditious a manner as possible, after testing them under field conditions; disabling all unused ports and services and assuring that they remain disabled; restricting IoT user privileges to only those that are required for each person’s role; tracking and monitoring audit trails; and using security controls such as antivirus software and file integrity checking software where technically feasible.
■ Preventing unauthorized modification of data. This includes data that are in transit (at least across the network boundaries) and at rest.
■ Detecting security events and incidents. The object is to detect security events early enough to break the attack chain before attackers attain their objectives. This includes the capability to detect failed IoT components, unavailable services, and exhausted resources that are important to provide proper and safe functioning of an IoT system.

## Slide 19: IoT Security Objectives
Maintaining functionality during adverse conditions
    This involves designing IoT systems so that each critical component has a redundant counterpart
    If a component fails, it should fail in a manner that does not generate unnecessary traffic on IoT or other networks, or does not cause another problem elsewhere
    IoT system should also allow for graceful degradation such as moving from normal operation with full automation to emergency operation with operators more involved and less automation to manual operation with no automation
Restoring the system after an incident
    Incidents are inevitable and an incident response plan is essential
    A major characteristic of a good security program is how quickly the IoT system can be recovered after an incident has occurred
Notes: ■ Maintaining functionality during adverse conditions. This involves designing IoT system so that each critical component has a redundant counterpart. Additionally, if a component fails, it should fail in a manner that does not generate unnecessary traffic on IoT or other networks, or does not cause another problem elsewhere. IoT system should also allow for graceful degradation such as moving from normal operation with full automation to emergency operation with operators more involved and less automation to manual operation with no automation.
■ Restoring the system after an incident. Incidents are inevitable and an incident response plan is essential. A major characteristic of a good security program is how quickly the IoT system can be recovered after an incident has occurred.

## Slide 20: Tamper Resistance and Detection
Tampering
An unauthorized modification that alters the intended functioning of a system or device in a way that degrades the security it provides
Tamper resistant
A characteristic of a system component that provides passive protection against an attack
Tamper detection
Techniques to ensure that the overall system is made aware of unwanted physical access
Notes: An IoT ecosystem involves a large number of devices deployed in the edge network and in the fog network. Typically these involve numerous manufacturers and multiple supply chains and often deployment in areas where physical security is difficult. Two essential security measures in such an environment are tamper resistance and tamper detection. We define the following terms:
  ■ Tampering: An unauthorized modification that alters the intended functioning of a system or device in a way that degrades the security it provides.
  ■ Tamper resistant: A characteristic of a system component that provides passive protection against an attack.
  ■ Tamper detection: Techniques to ensure that the overall system is made aware of unwanted physical access.

## Slide 21: Tamper Resistance
The common approach to tamper resistance is to use specialized physical construction materials to make tampering with a fog node difficult
    Examples include hardened steel enclosures, locks, and security screws
A second category of tamper resistance is the deterrence of tampering by ensuring that tampering leaves visible evidence behind
    Examples include special seals and tapes that make it obvious when there has been physical tampering
Notes: The common approach to tamper resistance is to use specialized physical construction materials to make tampering with a fog node difficult. Examples include hardened steel enclosures, locks, and security screws. Tightly packing components and circuit boards within an enclosure increases the difficulty of using fiber optics to probe inside the node without opening the enclosure.
A second category of tamper resistance is the deterrence of tampering by ensuring that tampering leaves visible evidence behind. Examples include special seals and tapes that make it obvious when there has been physical tampering.

## Slide 22: Tamper Detection
Mechanisms for tamper detection include:
Switches
    A variety of switches, such as mercury switches, magnetic switches, and pressure contacts can detect the opening of a device, the breach of a physical security boundary, or the movement of a device
Sensors
    Temperature and radiation sensors can detect environmental changes. Voltage and power sensors can detect electrical attacks
Circuitry
    It is possible to wrap components with flexible circuitry, resistance wire, or fiber optics so as to detect a puncture or break
Notes: Mechanisms for tamper detection include the following:
■ Switches: A variety of switches, such as mercury switches, magnetic switches, and pressure contacts can detect the opening of a device, the breach of a physical security boundary, or the movement of a device.
■ Sensors: Temperature and radiation sensors can detect environmental changes. Voltage and power sensors can detect electrical attacks.
■ Circuitry: It is possible to wrap components with flexible circuitry, resistance wire, or fiber optics so as to detect a puncture or break.

## Slide 23: Security Requirements
Communication security:
Secure, trusted, and privacy-protected communication capability is required so that unauthorized access to the content of data can be prohibited, integrity of data can be guaranteed, and privacy-related content of data can be protected during data transmission or transfer in IoT
Data management security:
Secure, trusted, and privacy-protected data management capability is required so that unauthorized access to the content of data can be prohibited, integrity of data can be guaranteed, and privacy-related content of data can be protected when storing or processing data in IoT
Service provision security:
Secure, trusted, and privacy-protected service provision capability is required, so that unauthorized access to service and fraudulent service provision can be prohibited and privacy information related to IoT users can be protected
Integration of security policies and techniques:
The ability to integrate different security policies and techniques is required to ensure a consistent security control over the variety of devices and user networks in IoT
Mutual authentication and authorization:
Before a device can access the IoT, mutual authentication and authorization between the device and IoT is required to be performed according to predefined security policies
Security audit:
Security audit is required to be supported in IoT. Any data access or attempt to access IoT applications are required to be fully transparent, traceable, and reproducible according to appropriate regulation and laws
Notes: ITU-T Recommendation Y.2066 (Common Requirements of the Internet of Things, June 2014) includes a list of security requirements for the IoT. This list is a useful baseline for understanding the scope of security implementation needed for an IoT deployment. The requirements are defined as being the functional requirements during capturing, storing, transferring, aggregating and processing the data of things, as well as to the provision of services which involve things. These requirements are related to all the IoT actors. The requirements are:
■ Communication security: Secure, trusted, and privacy-protected communication capability is required, so that unauthorized access to the content of data can be prohibited, integrity of data can be guaranteed, and privacy-related content of data can be protected during data transmission or transfer in IoT.
■ Data management security: Secure, trusted, and privacy-protected data management capability is required, so that unauthorized access to the content of data can be prohibited, integrity of data can be guaranteed, and privacy-related content of data can be protected when storing or processing data in IoT.
■ Service provision security: Secure, trusted, and privacy protected service provision capability is required, so that unauthorized access to service and fraudulent service provision can be prohibited and privacy information related to IoT users can be protected.
■ Integration of security policies and techniques: The ability to integrate different security policies and techniques is required, so as to ensure a consistent security control over the variety of devices and user networks in IoT.
■ Mutual authentication and authorization: Before a device (or an IoT user) can access the IoT, mutual authentication and authorization between the device (or the IoT user) and IoT is required to be performed according to predefined security policies.
■ Security audit: Security audit is required to be supported in IoT. Any data access or attempt to access IoT applications are required to be fully transparent, traceable, and reproducible according to appropriate regulation and laws. In particular, IoT is required to support security audit for data transmission, storage, processing, and application access.

## Slide 24
Notes: A key element in providing security in an IoT deployment is the gateway. Y.2067 (Common Requirements and Capabilities of a Gateway for Internet of Things Applications, June 2014) details specific security functions that the gateway should implement, some of which are illustrated in Figure 23.4. These consist of the following:
■ Support identification of each access to the connected devices.
■ Support authentication with devices. Based on application requirements and device capabilities, it is required to support mutual or one-way authentication with devices. With one-way authentication, either the device authenticates itself to the gateway or the gateway authenticates itself to the device, but not both.
■ Support mutual authentication with applications.
■ Support the security of the data that are stored in devices and the gateway, or transferred between the gateway and devices, or transferred between the gateway and applications. Support the security of these data based on security levels.
■ Support mechanisms to protect privacy for devices and the gateway.
■ Support self-diagnosis and self-repair as well as remote maintenance.
■ Support firmware and software update.
■ Support auto configuration or configuration by applications. The gateway is required to support multiple configuration modes, e.g., remote and local con- figuration, automatic and manual configuration, and dynamic configuration based on policies.
Some of these requirements may be difficult to achieve when they involve providing security services for constrained devices. For example, the gateway should support security of data stored in devices. Without encryption capability at the constrained device, this may be impractical to achieve.
Note that the Y.2067 requirements make a number of references to privacy requirements. Privacy is an area of growing concern with the widespread deployment of IoT-enabled things in homes, retail outlets, and vehicles and humans. As more things are interconnected, governments and private enterprises will collect massive amounts of data about individuals, including medical information, location and movement information, and application usage.

## Slide 25
Notes: Figure 23.5 models the scope of key security capabilities across the four levels of the IoT ecosystem:
■ User authentication and access control: These functions span then entire IoT ecosystem. A common approach to access control is role-based access control (RBAC). RBAC systems assign access rights to roles instead of individual users. In turn, users are assigned to different roles, either statically or dynamically, according to their responsibilities. RBAC enjoys widespread commercial use in cloud and enterprise systems and is a well-understood tool that can be used to manage access to IoT devices and the data they generate.
■ Tamper resistance and detection: This function is particularly important at the device and fog network levels but also extends to the core network level. All of these levels may involve components that are physically outside the area of the enterprise that is protected by physical security measures.
■ Data protection and confidentiality: These functions extend to all levels of the architecture.
■ Internet protocol and network security: Protection of data in motion from eavesdropping and snooping is essential between all levels.

## Slide 26: MiniSec
An open-source security module that is part of the TinyOS operating system
    TinyOS is designed for small embedded systems with tight requirements on memory, processing time, real-time response, and power consumption
    MiniSec is designed to be a link-level module that offers a high level of security, while simultaneously keeping energy consumption low and using very little memory
    MiniSec provides confidentiality, authentication, and replay protection
Notes: This section provides an overview of MiniSec, an open-source security module that is part of the TinyOS operating system. TinyOS is designed for small embedded systems with tight requirements on memory, processing time, real-time response, and power consumption. TinyOS takes the process of streamlining quite far, resulting in a very minimal OS for embedded systems, with a typical configuration requiring 48 KB of code and 10 KB of RAM [LEVI12]. The main application of TinyOS is wireless sensor networks and it has become the de facto OS for such networks. With sensor networks, the primary security concerns relate to wireless communications. MiniSec is designed to be a link-level module that offers a high level of security, while simultaneously keeping energy consumption low and using very little memory [LUK07]. MiniSec provides confidentiality, authentication, and replay protection.

## Slide 27: MiniSec
MiniSec has two operating modes:
    One tailored for single-source communication
    One tailored for multi-source broadcast communication
MiniSec is designed to meet the following requirements:
    Data authentication
    Confidentiality
    Replay protection
    Freshness
    Low energy overhead
    Resilient to lost messages
Notes: MiniSec has two operating modes, one tailored for single-source communication, and another tailored for multi-source broadcast communication. The latter does not require per-sender state for replay protection and thus scales to large networks.
MiniSec is designed to meet the following requirements:
■ Data authentication: Enables a legitimate node to verify whether a message originated from another legitimate node (i.e., a node with which it shares a secret key) and was unchanged during transmission.
■ Confidentiality: A basic requirement for any secure communications system.
■ Replay protection: Prevents an attacker from successfully recording a packet and replaying it at a later time.
■ Freshness: Because sensor nodes often stream time-varying measurements, providing guarantee of message freshness is an important property. There are two types of freshness: strong freshness and weak freshness. MiniSec provides a mechanism to guarantee weak freshness, where a receiver can determine a partial ordering over received messages without a local reference time point.
■ Low energy overhead: This is achieved by minimizing communication over- head and by the use of only symmetric.
■ Resilient to lost messages: The relatively high occurrence of dropped packets in wireless sensor networks requires a design that can tolerate high message loss rates.

## Slide 28: Skipjack
Encryption algorithm used by MiniSec
Was developed in the 1990s by the U.S. National Security Agency (NSA)
Is one of the simplest and fastest block cipher algorithms, which is critical to embedded systems
Makes use of an 80-bit key
With its efficient computation and low memory footprint, Skipjack is an attractive choice for IoT devices
Notes: Two cryptographic algorithms used by MiniSec are worth noting. The first of these is the encryption algorithm Skipjack. Skipjack was developed in the 1990s by the U.S. National Security Agency (NSA). It is one of the simplest and fastest block cipher algorithms, which is critical to embedded systems. A study of eight possible candidate algorithms for wireless security networks [LAW06] concluded that Skipjack was the best algorithm in terms of code memory, data memory, encryption/decryption efficiency, and key setup efficiency.
Skipjack makes use of an 80-bit key. It was intended by NSA to provide a secure system once it became clear that DES, with only a 56-bit key, was vulnerable. Contemporary algorithms, such as AES, employ a key length of at least 128 bits, and 80 bits is generally considered inadequate. However, for the limited application of wireless sensor networks and other IoT devices, which provide large volumes of short data blocks over a slow data link, Skipjack may suffice. With its efficient computation and low memory footprint, Skipjack is an attractive choice for IoT devices. However, going forward, it is advisable for any IoT security module to use one of the recently developed lightweight cryptographic algorithms, such as the Scalable Encryption Algorithm (SEA) described in Chapter 14.

## Slide 29: Operating Modes
MiniSec has two operating modes: unicast (MiniSec-U) and broadcast (MiniSec-B)
Both schemes use OCB with a counter that is input along with the plaintext into the encryption algorithm
The least significant bits of the counter are also sent as plaintext to enable synchronization
For both modes, data are transmitted in packets
Each packet includes the encrypted data block, the OCB authentication tag, and the MiniSec counter
MiniSec-U employs synchronized counters, which require the receiver to keep a local counter for each sender
Once a receiver observes a counter value, it rejects packets with an equal or smaller counter value; therefore, an attacker cannot replay any packet that the receiver has previously received
Notes: MiniSec has two operating modes: unicast (MiniSec-U) and broadcast (MiniSec-B). Both schemes use OCB with a counter, known as a nonce, that is input along with the plaintext into the encryption algorithm. The least significant bits of the counter are also sent as plaintext to enable synchronization. For both modes, data are trans- mitted in packets. Each packet includes the encrypted data block, the OCB authentication tag, and the MiniSec counter.
MiniSec-U employs synchronized counters, which require the receiver to keep a local counter for each sender. The strictly monotonically increasing counter guarantees semantic confidentiality. Even if the sender A repeatedly sends the same message, each ciphertext is different since a different counter value is used. Also, once a receiver observes a counter value, it rejects packets with an equal or smaller counter value. Therefore, an attacker cannot replay any packet that the receiver has previously received. If a number of packets are dropped, the sender and receiver engage in a resynchronization protocol.

## Slide 30: Operating Modes
MiniSec-U cannot be directly used to secure broadcast communication
    It would be too expensive to run the counter resynchronization protocol among many receivers
    If a node were to simultaneously receive packets from a large group of sending nodes, it would need to maintain a counter for each sender, resulting in high memory overhead
Instead, it uses two mechanisms, a timing-based approach and a bloom-filter approach, that defend against replay attacks
The timing approach is augmented with a bloom-filter approach in order to prevent replay attacks inside the current epoch
Every time that a node receives a message, it checks if it belongs to its bloom filter
If the message is not replayed, it is stored in the bloom filter; else, the node drops it
Notes: MiniSec-U cannot be directly used to secure broadcast communication. First, it would be too expensive to run the counter resynchronization protocol among many receivers. Also, if a node were to simultaneously receive packets from a large group of sending nodes, it would need to maintain a counter for each sender, resulting in high memory overhead. Instead, it uses two mechanisms, a timing-based approach and a bloom-filter approach, that defend against replay attacks. First, the time is divided into t-length epochs E1, E2,. . . . Using the current epoch or the previous epoch as nonce for OCB encryption, the replay of messages from older epochs is avoided. The timing approach is augmented with a bloom-filter approach in order to prevent replay attacks inside the current epoch. MiniSec-B uses as nonce element in OCB encryption and bloom-filter key the string nodeID.Ei.Cab, where nodeID is the sender node identifier, Ei is the current epoch, and Cab is a shared counter. Every time that a node receives a message, it checks if it belongs to its bloom filter. If the message is not replayed, it is stored in the bloom filter. Else, the node drops it.

## Slide 31
Notes: As mentioned in Chapter 7, a mode of operation must be specified when a plaintext source consists of multiple blocks of data to be encrypted with the same encryption key. OCB is an NIST proposed block cipher mode of operation [ROGA01], and is a proposed Internet Standard defined in RFC 7253 (The OCB Authenticated-Encryption Algorithm, May 2014). OCB is also approved as an authenticated encryption technique in the IEEE 802.11 wireless LAN standard. And, OCB is included in MiniSec, an open-source IoT security module.
A key objective for OCB is efficiency. This is achieved by minimizing the number of encryptions required per message and by allowing for parallel operation on the blocks of a message. OCB mode is provably secure assuming the underlying block cipher is secure. OCB mode is a one-pass mode of operation making it highly efficient. Only one block cipher call is necessary for each plaintext block, with an additional two calls needed to complete the whole encryption process. OCB is especially well suited for the stringent energy constraints of sensor nodes.
Figure 23.6 shows the overall structure for OCB encryption and authentication.
Note that the encryption structure for OCB is similar to that of electronic codebook (ECB) mode. Each block is encrypted independently of the other blocks, so that it is possible to perform all m encryptions simultaneously.

## Slide 32
Notes: Figure 23.7 summarizes the OCB algorithms for encryption and decryption.

## Slide 33: Summary
Explain the scope of the Internet of Things
List and discuss the five principal components of IoT-enabled things
Understand the relationship between cloud computing and IoT
Define the patching vulnerability
Explain the IoT Security Framework
Understand the MiniSec security feature for wireless sensor networks
Notes: Chapter 23 summary.